## Slide 1: A Hard X-Ray Free-Electron Laser Oscillator at the European XFEL facility
Diamond Crystals
Grazing Incidence Optics
Bending Magnets
─ electron orbit
─ photons
Immo Bahns, Patrick Rauer,
- W. Decking, J. Rossbach, H. Sinn –
Joint RD meeting
supported by BMBF FKZ 05K16GU4

## Slide 2: XFELO Basic Concept
X-ray FEL Oscillator:
  Suggestion by K.J. Kim 2008: use principle of Bragg reflection
Bragg‘s law:
Notes: FELO  UV to IR optical with high reflectivity based on Fresnel equations are available
XFELO  wavelength in range of atomic distance  reflectivity based on Fresnel equations is very small  X-ray optics: Bragg reflector, Grazing incident mirror, Gratings
Dynamical diffraction theory  Bandwidth of Bragg reflector is finite

## Slide 3: XFELO at EuropeanXFEL
XFELO necessities:
-High enough single pass gain to compensate for losses
Brilliant electron beam (Linac)
  Matching between electron bunch repitition and photon pulse round trip rate
    F.E. LCLS : el. rep-rate = 120 Hz↔2500 km optical path length
euXFEL: el. rep-rate ~ 2.25 MHz ↔ 66.42m reflector distance
Implement a proof-of-principle XFELO at the end of the SASE1 tunnel (last 4-6 Undulators)
Keep it simple (no fancy outcoupling schemes, no tunability, two(four) thick mirrors, compliant with standard operation)
Project proposal in preperation
Notes: Was zeichnet einen „Brilliant electron beam“ aus? Warum ist diesbezüglich Linac besser als Speicherring?

## Slide 4: Feasible Parameters
[1] G. Geloni et al., N. Jour. Phys., 12, 035021 (2010)
XFELO:
  Pulseenergy ~ 2mJ
  Pulse lengths of ~ 150fs
  Bandwidth
  Full pulse coherence
  Application Energy resolved measurements/ measurements requiring coherence!
Notes: SASE (213m)  undulator length 213m?
SASE data simulation or measurement?
High powers SASE  few tens of mJ
High powers XFELO  outcoupling of a few mJ in cavity
-0.2 fs ->multimode interference
-150fs ->fourierlimit pulse duration
Energy resolved measurements  Example: absorption edges, Example for single-frequency X-ray source measurement
Photon puls länger als -> electropuls

## Slide 5: XFELO Plans at SASE1
Implement a proof-of-principle XFELO at the end of the SASE1 tunnel (last 4 Undulators)
Parameters for XFELO setup/Simulation:
  electron energy = 16GeV
  electron repetition-rate =2.25MhZ
  mirror to mirror distance =66.42m
  mirror material: Diamant
  Bragg energies: 6.967 keV (4 0 0 reflex)
  Mirror thickness: both 150µm
  focusing grazing incidence mirror with (in both transverse planes)
  Standard electron bunches Q=250pC, rms bunch length = 20 fs, Peak current = 5kA

## Slide 6: Assuming no errors (and no heat load)
First pass:
  strong synchrotron radiation background
  thousand of longitudinal modes which in transverse space average to a quasi-gaussian distribution

## Slide 7: Assuming no errors, no effective aperture (and no heat load)
Only one longitudianal mode refected:
  quasi-gaussian transverse properties loss (no averaging of the long. Modes)
  radiation profile will then seed the next electron pulse

## Slide 8: Assuming no errors, no effective aperture (and no heat load)
After three round trips:
  a strong seeding close to the Bragg energy
  seed dominate over the SASE
  Transverse distribution becomes more gaussian like due to the strong gain guiding
After ten round trips:

## Slide 9: Assuming no errors, no effective aperture (and no heat load)
In cavity after twenty round trips  saturated:
outcoupeled after twenty round trips  saturated:

## Slide 10: Assuming no errors, no effective aperture (and no heat load)

## Slide 11: Assuming errors (and no heat load)
  Including:
  cavity quality factor = 0.95
  including a mirror tilt of Θ_r≈100nrad
  rms electron pointing jitter = 80nrad
  arrival time jitter = 20fs
  surprisingly negligible effects
  overall energy in saturation is even slightly higher
  angular jitter leading to an averaging out of the inherent electron bunch orbital errors
No errors

## Slide 12: XFELO  Heatload Issues
mJ pulse
Bragg-reflector
Saturated XFELO  4mJ at >1MHz rep.rate on crystal
    Disturbing optical stability  (long term) vibrations
    Disturbing crystal spectral reflectivity
Thermal expansion of the lattice in the region of interest:
Dynamics Answer Of Crystal Towards Rapid Expansion  Strain Waves (Ultrasonics):
Implemented in Simulations  results on the next sheets
Influence unknown todate  checked by simulation as well as by experiment
 Not yet implemented

## Slide 13: Interaction of Electromagnetic radiation with Bragg reflectors
Michelson Interferometer:
Photodiode (risetime<175ps) measures intensity proportional to|E|2 of the probe CW laser (532nm)
For a maximum effect of interference the same polarization is needed and equal intensities
Stabilization of working (WP) point with PID controller
Displacement << ¼ λ signal (intensity) is proportional to displacement
Averaging over thousands of pulses
Resolution <0.5 pm
Imess [mV]
WP
0 λ/4 λ/2
Δz
Problem: “Simple” Fourier-Law (infinite speed of heat propagation) will fail at low temperatures
Challenging Part:
Find proper theoretical-model for Thermoelectricity simulation and solve it: Fourier-Law, Cattaneo-equation, Boltzmann transport equation
Solving analytical or Numerical:
FEM, FVM, Monte-Carlo
Pump-Probe Measurments:
Beanchmark for Simulation  Find a theoretical-model that is accurate and fast to solve

## Slide 14: Interaction of Electromagnetic radiation with Bragg reflectors
Experimental Setup:
Pump-Probe measurements
Pump: Pulsed UV Laser  similar heat load like saturated XFELO radiation
Probe: CW-Laser + Ultrafast Photodiods (GHz)
Methods:
Michelson-Interferometer  Displacement
Thermoreflectance  Measuring transient change of reflectance  refractive index (susceptibility)
Knife-Edge-Method  Measuring angular changes surface waves
Imess [mV]
WP
0 λ/4 λ/2
Δz
Technical Problems:
Vacuum level <10E-8
high frequency signals

## Slide 15: Interaction of Electromagnetic radiation with Bragg reflectors
Imess [mV]
WP
0 λ/4 λ/2
Δz
First Results:
Resolution
<0.5 pm

## Slide 16: XFELO + Heat Load (no dynamical strain)
Same conditions as before but crystals cooled down to 77K (nitrogen cooling)
Heat simulation  radial symmetric FEM Simulation after each photon pulse
Take the averaged temperature after 440ns (next pulse arrives) input for shift of refection curve
High thermal diffusion at 77K for diamond  homogeneous temperature after 400ns
Stable operation  if heat transfer to holder is sufficient and theoretical model valid

## Slide 17: XFELO + Heat Load (no dynamical strain)
Quick and dirty simulation for heat load at room temperature  Same procedure as before
averaged temperature after 440ns (next pulse arrives) input for shift of refection curve  homogeneous temperature after 400ns  not true for room temperature thermal diffusion
XFELO still seeds but no stable saturation
  Different spot size on crystal  different shift of the reflectivity curves
  gap between ref. curves to big  not seed  crystal cools  gap decreases  seed starts again

## Slide 18: Conclusion
European XFEL ideal source for implementing an XFELO
Problems:
  Heatload  Stability at saturation
Need to try it out  Proof of principle experiment
Thank you for listening